## Slide 1: Transport Layer CS 3516 – Computer Networks

## Slide 2: Chapter 3: Transport Layer
Goals:
Understand principles behind transport layer services:
  Multiplexing / demultiplexing
  Reliable data transfer
  Flow control
  Congestion control
Learn about transport layer protocols in the Internet:
  UDP: connectionless transport
  TCP: connection-oriented transport
  TCP congestion control

## Slide 3: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 4: Transport Services and Protocols
Provide logical communication between app processes running on different hosts
Transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  receive side: reassembles segments into messages, passes to app layer
More than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 5: Transport vs. Network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
Household analogy:
12 kids sending letters to 12 kids
processes = kids
app messages = letters in envelopes
hosts = houses
transport protocol = Ann and Bill (collect mail from siblings)
network-layer protocol = postal service

## Slide 6: Internet Transport-layer Protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 7: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 8: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 9: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
Finer application control over data
No connection establishment
No connection state
Smaller packet overhead

## Slide 10: UDP: more
Often used for streaming (video/audio) or game apps
  loss tolerant
  rate sensitive
other UDP uses
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 11: UDP: checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 12: Internet Checksum Example
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
At receiver, add 2 integers and checksum … should be all 1’s. If not, bit error (correction?  next)
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 13: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 14: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 15: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 16: Principles of Reliable Data Transfer
important in app., transport, link layers
top-10 list of important networking topics!
Characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
(Zoom next slide)

## Slide 17: Reliable Data Transfer: Getting Started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 18: Reliable Data Transfer: Getting Started
We’ll:
Incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
Consider only unidirectional data transfer
  but control info will flow on both directions!
Use finite state machines (FSM) to specify sender, receiver
state 1
state 2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 19: Rdt1.0: Reliable Transfer over a Reliable Channel
Underlying channel perfectly reliable
  no bit errors
  no loss of packets
Separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver
Easy!

## Slide 20: What if Taking a Message over Phone?
Message is clear?
Message is garbled?

## Slide 21: What if Taking a Message over Phone?
Message is clear?
  Ok
Message is garbled?
  Ask to repeat
  May not need whole message
In networks, called Automatic Repeat reQuest (ARQ)
  Need error detection
  Receiver feedback
  Retransmission

## Slide 22: Rdt2.0: Channel with Bit Errors (no Loss)
Underlying channel may flip bits in packet
  Checksum to detect bit errors
The question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  Sender retransmits pkt on receipt of NAK
New mechanisms in rdt2.0 (beyond rdt1.0):
  Error detection
  Receiver feedback: control msgs (ACK,NAK) rcvrsender

## Slide 23: Rdt2.0: FSM Specification
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 24: Rdt2.0: Operation with No Errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
sender
receiver

## Slide 25: Rdt2.0: Error Scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L
sender
receiver
Sender sends one packet,
then waits for receiver
response
stop and wait

## Slide 26: Rdt2.0 Has a Fatal Flaw!
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L
???

## Slide 27: Rdt2.0 Has a Fatal Flaw!
What happens if ACK/NAK corrupted?
Sender doesn’t know what happened at receiver!
Can’t just retransmit: possible duplicate
How to handle duplicates?

## Slide 28: Rdt2.0 Has a Fatal Flaw!
What happens if ACK/NAK corrupted?
Sender doesn’t know what happened at receiver!
Can’t just retransmit: possible duplicate
Handling duplicates:
Sender retransmits current pkt if ACK/NAK garbled
Sender adds sequence number to each pkt
  Can use 1 bit (for now)
receiver discards (doesn’t deliver up) duplicate pkt

## Slide 29: Rdt2.1: Sender, Handles Garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 30: Rdt2.1: Receiver, Handles Garbled ACK/NAKs
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)

## Slide 31: Rdt2.1: Discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will suffice
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 32: Rdt2.2: a NAK-free Protocol
Reduce type of response  ACK only
Same functionality as rdt2.1, using ACKs only
Instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
Duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 33: Rdt2.2: Sender & Receiver Fragments
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK 0
sender FSM
fragment
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 34: Rdt3.0: Channels with Errors and Loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
How to determine if a packet is lost?

## Slide 35: Rdt3.0: Channels with Errors and Loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
Retransmits if no ACK received in this time
If pkt (or ACK) just delayed (not lost):
  Retransmission will be duplicate, but use of seq. #’s already handles this
  Receiver must specify seq # of pkt being ACKed
Requires countdown timer

## Slide 36: Rdt3.0 Sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 37: Rdt3.0 in Action

## Slide 38: Rdt3.0 in Action

## Slide 39: Performance of Rdt3.0
Rdt3.0 works, but performance stinks…
ex: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  U sender: utilization – fraction of time sender busy sending
  1KB pkt every 30 msec -> 33kB/sec throughput over 1 Gbps link
  Network protocol limits use of physical resources!
(Picture next slide)

## Slide 40: Rdt3.0: Stop-and-Wait Operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 41: Pipelined Protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  Range of sequence numbers must be increased
  Need buffering at sender and/or receiver

## Slide 42: Pipelining: Increased Utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!
Two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 43: Pipelining Protocols
Go-back-N: overview
sender: up to N unACKed pkts in pipeline
receiver: only sends cumulative ACKs
  doesn’t ACK pkt if there’s a gap
sender: has timer for oldest unACKed pkt
  if timer expires: retransmit all unACKed packets
Selective Repeat: overview
sender: up to N unACKed packets in pipeline
receiver: ACKs individual pkts
sender: maintains timer for each unACKed pkt
  if timer expires: retransmit only unACKed packet

## Slide 44: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unACKed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
Timer for each in-flight pkt
Timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 45: GBN: Sender Extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 46: GBN: Receiver Extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L

## Slide 47: GBN in action

## Slide 48: GBN Applet!
http://media.pearsoncmg.com/aw/aw_kurose_network_4/applets/go-back-n/index.html

## Slide 49: Selective Repeat
Receiver individually acknowledges all correctly received pkts
  Buffers pkts, as needed, for eventual in-order delivery to upper layer
Sender only resends pkts for which ACK not received
  Sender timer for each unACKed pkt
Sender window
  N consecutive seq #’s
  Again limits seq #s of sent, unACKed pkts

## Slide 50: Selective Repeat: sender, receiver windows

## Slide 51: Selective Repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 52: Selective Repeat in Action

## Slide 53: Selective Repeat: Dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
incorrectly passes duplicate data as new in (a)
Q: what relationship between seq # size and window size?

## Slide 54: SR Applet!
http://media.pearsoncmg.com/aw/aw_kurose_network_4/applets/SR/index.html

## Slide 55: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 56: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 57: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 59: TCP Seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say  up to implementer
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
time
simple telnet scenario
host ACKs
receipt of
‘C’, echoes
back ‘C’

## Slide 60: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?

## Slide 61: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
Longer than RTT
  but RTT varies
Too short? premature timeout
  unnecessary retransmissions
Too long? slow reaction to segment loss
Q: how to estimate RTT?

## Slide 62: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
Longer than RTT
  but RTT varies
Too short? premature timeout
  unnecessary retransmissions
Too long? slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 63: TCP Round Trip Time and Timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 1/8th (or 0.125)

## Slide 64: Example Round Trip Time Estimation

## Slide 65: TCP Round Trip Time and Timeout
Setting the timeout
EstimtedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
First estimate of how much SampleRTT deviates from EstimatedRTT:
TimeoutInterval = EstimatedRTT + 4*DevRTT
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
Then set timeout interval:

## Slide 66: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 67: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
Pipelined segments
Cumulative ACKs
TCP uses single retransmission timer
Retransmissions are triggered by:
  Timeout events
  Duplicate ACKs
Initially consider simplified TCP sender:
  Ignore duplicate ACKs
  Ignore flow control, congestion control

## Slide 68: TCP Sender Events:
Data rcvd from app:
Create segment with seq #
seq # is byte-stream number of first data byte in segment
Start timer if not already running (think of timer as for oldest unACKed segment)
Expiration interval: TimeOutInterval
Timeout:
retransmit segment that caused timeout
restart timer
ACK rcvd:
If acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are outstanding segments

## Slide 69: TCP Sender (simplified)
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
loop (forever) {
switch(event)
event: data received from application above
create TCP segment w/seq # NextSeqNum
if (timer currently not running)
start timer
pass segment to IP
NextSeqNum = NextSeqNum + length(data)
event: timer timeout
retransmit not-yet-acked segment with
smallest sequence number
start timer
event: ACK received, with ACK field value of y
if (y > SendBase) {
SendBase = y
if (there are not-yet-acked segments)
start timer
}
} /* end of loop forever */
Comment:
SendBase-1: last
cumulatively ACKed byte
Example:
SendBase-1 = 71; y= 73, so the rcvr wants 73+ ; y > SendBase, so that new data is ACKed

## Slide 70: TCP: Retransmission Scenarios
Host A
Seq=100, 20 bytes data
ACK=100
time
premature timeout
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=92 timeout
ACK=120
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
time
Seq=92 timeout
SendBase
= 100
SendBase
= 120
SendBase
= 120
Sendbase
= 100

## Slide 71: TCP Retransmission Scenarios (more)
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
Cumulative ACK scenario
Host B
X
Seq=100, 20 bytes data
ACK=120
time
SendBase
= 120

## Slide 72: TCP ACK generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap

## Slide 73: Fast Retransmit
Time-out period often relatively long:
  Long delay before resending lost packet
Detect lost segments via duplicate ACKs
  Sender often sends many segments back-to-back
  If segment lost, there will likely be many duplicate ACKs for that segment
If sender receives 3 ACKs for same data, it assumes that segment after ACKed data was lost:
  fast retransmit: resend segment before timer expires

## Slide 74: Fast Retransmit
Host A
timeout
Host B
time
X
resend seq X2
seq # x1
seq # x2
seq # x3
seq # x4
seq # x5
ACK x1
ACK x1
ACK x1
ACK x1
triple
duplicate
ACKs

## Slide 75: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 76: TCP Flow Control
Receive side of TCP connection has a receive buffer:
speed-matching service: matching send rate to receiving application’s drain rate
App process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control
IP
datagrams
TCP data
(in buffer)
(currently)
unused buffer
space
application
process

## Slide 77: TCP Flow Control: How it Works
(suppose TCP receiver discards out-of-order segments)
unused buffer space:
= rwnd
= RcvBuffer-[LastByteRcvd - LastByteRead]
Receiver: advertises unused buffer space by including rwnd value in segment header
sender: limits # of unACKed bytes to rwnd
  guarantees receiver’s buffer doesn’t overflow
IP
datagrams
TCP data
(in buffer)
(currently)
unused buffer
space
application
process
rwnd
RcvBuffer

## Slide 78: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 79: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info (e.g. RcvWindow)
client: connection initiator
Socket clientSocket = new Socket(“hostname”, port#);
server: contacted by client
Socket connectionSocket = welcomeSocket.accept();
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies initial seq #
  no data
Step 2: server host receives SYN, replies with SYNACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data

## Slide 80: TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 81: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 82: TCP Connection Management (cont.)
TCP client
lifecycle
TCP server
lifecycle

## Slide 83: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 84: Principles of Congestion Control
Congestion:
Informally: “too many sources sending too much data too fast for network to handle”
Different from flow control!
Manifestations:
  Lost packets (buffer overflow at routers)
  Long delays (queueing in router buffers)
A “top-10” problem!

## Slide 85: Causes/costs of Congestion: Scenario 1
Two senders, two receivers
One router, infinite buffers
No retransmission
Large delays when congested
Maximum achievable throughput
unlimited shared output link buffers
Host A
lin : original data
Host B
lout

## Slide 86: Causes/costs of Congestion: Scenario 2
One router, finite buffers
Sender retransmission of lost packet
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in : original data, plus retransmitted data

## Slide 87: Causes/costs of congestion: Scenario 2
Always: (goodput)
“Perfect” retransmission only when loss:
Retransmission of delayed (not lost) packet makes larger (than perfect case) for same
l
in
l
out
=
l
in
l
out
>
l
in
l
out
“Costs” of congestion:
More work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
R/2
R/2
lin
lout
b.
R/2
R/2
lin
lout
a.
R/2
R/2
lin
lout
c.
R/4
R/3

## Slide 88: Causes/costs of Congestion: Scenario 3
Four senders
Multihop paths
Timeout/retransmit
l
in
Q: what happens as and increase ?
l
in
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in : original data, plus retransmitted data

## Slide 89: Causes/costs of Congestion: Scenario 3
Another “cost” of congestion:
When packet dropped, any “upstream transmission capacity used for that packet was wasted!
Host A
Host B
lout

## Slide 90: Approaches towards congestion control
End-end congestion control:
No explicit feedback from network
Congestion inferred from end-system observed loss, delay
Approach taken by TCP
Network-assisted congestion control:
Routers provide feedback to end systems
  Single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  Explicit rate sender should send at
Broadly:

## Slide 91: Network assisted congestion control

## Slide 92: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 93: TCP Congestion Control:
Goal: TCP sender should transmit as fast as possible, but without congesting network
  Q: how to find rate just below congestion level?
Decentralized: each TCP sender sets its own rate, based on implicit feedback:
  ACK: segment received (a good thing!), network not congested, so increase sending rate
  lost segment: assume loss due to congested network, so decrease sending rate

## Slide 94: TCP Congestion Control: Bandwidth Probing
“Probing for bandwidth”: increase transmission rate on receipt of ACK, until eventually loss occurs, then decrease transmission rate
  continue to increase on ACK, decrease on loss (since available bandwidth is changing, depending on other connections in network)
ACKs being received,
so increase rate
X
X
X
X
X
loss, so decrease rate
sending rate
time
Q: how fast to increase/decrease?
  details to follow
TCP’s
“sawtooth”
behavior

## Slide 95: TCP Congestion Control: details
sender limits rate by limiting number of unACKed bytes “in pipeline”:
  cwnd: differs from rwnd (how, why?)
  sender limited by min(cwnd,rwnd)
roughly,
cwnd is dynamic, function of perceived network congestion
rate =
cwnd
RTT
bytes/sec
LastByteSent-LastByteAcked  cwnd
cwnd
bytes
RTT
ACK(s)

## Slide 96: TCP Congestion Control: more details
segment loss event: reducing cwnd
timeout: no response from receiver
  cut cwnd to 1
3 duplicate ACKs: at least some segments getting through (recall fast retransmit)
  cut cwnd in half, less aggressively than on timeout
ACK received: increase cwnd
slowstart phase:
  increase exponentially fast (despite name) at connection start, or following timeout
congestion avoidance:
  increase linearly

## Slide 97: TCP Slow Start
when connection begins, cwnd = 1 MSS
  example: MSS = 500 bytes & RTT = 200 msec
  initial rate = 20 kbps
available bandwidth may be >> MSS/RTT
  desirable to quickly ramp up to respectable rate
increase rate exponentially until first loss event or when threshold reached
  double cwnd every RTT
  done by incrementing cwnd by 1 for every ACK received
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 98: Transitioning into/out of slowstart
ssthresh: cwnd threshold maintained by TCP
on loss event: set ssthresh to cwnd/2
  remember (half of) TCP rate when congestion last occurred
when cwnd >= ssthresh: transition from slowstart to congestion avoidance phase
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s),as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
congestion
avoidance

## Slide 99: TCP: Congestion Avoidance
When cwnd > ssthresh grow cwnd linearly
  increase cwnd by 1 MSS per RTT
  approach possible congestion slower than in slowstart
  implementation: cwnd = cwnd + MSS/cwnd for each ACK received
ACKs: increase cwnd by 1 MSS per RTT: additive increase
loss: cut cwnd in half (non-timeout-detected loss ): multiplicative decrease
AIMD
AIMD: Additive Increase
Multiplicative Decrease

## Slide 100: TCP Congestion Control FSM: overview
slow
start
congestion
avoidance
fast
recovery
cwnd > ssthresh
loss:
timeout
loss:
timeout
new ACK
loss:
3dupACK
loss:
3dupACK
loss:
timeout

## Slide 101: Popular “flavors” of TCP
ssthresh
ssthresh
TCP Tahoe
TCP Reno
Transmission round
cwnd window size (in segments)

## Slide 102: Summary: TCP Congestion Control
when cwnd < ssthresh, sender in slow-start phase, window grows exponentially.
when cwnd >= ssthresh, sender is in congestion-avoidance phase, window grows linearly.
when triple duplicate ACK occurs, ssthresh set to cwnd/2, cwnd set to ~ ssthresh
when timeout occurs, ssthresh set to cwnd/2, cwnd set to 1 MSS.

## Slide 103: TCP throughput
Q: what’s average throughout of TCP as function of window size, RTT?
  ignoring slow start
Let W be window size when loss occurs.
  when window is W, throughput is W/RTT
  just after loss, window drops to W/2, throughput to W/2RTT.
  average throughout: .75 W/RTT

## Slide 104: TCP Futures: TCP over “long, fat pipes”
Example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
Requires window size W = 83,333 in-flight segments!
throughput in terms of loss rate:
➜ L = 2·10-10 Wow
New versions of TCP for high-speed

## Slide 105: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP
connection 2

## Slide 106: Why is TCP fair?
Two competing sessions:
Additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 107: Fairness (more)
Fairness and UDP
Multimedia apps often do not use TCP
  do not want rate throttled by congestion control
Instead use UDP:
  pump audio/video at constant rate, tolerate packet loss
Fairness and Parallel TCP Connections
Nothing prevents app from opening parallel connections between 2 hosts.
Web browsers do this
Example: link of rate R supporting 9 connections;
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2 !

## Slide 108: Chapter 3: Summary
Principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
Instantiation and implementation in the Internet
  UDP
  TCP
Next:
leaving the network “edge” (application, transport layers)
into the network “core”